| Document Title: | How to integrate LSI based controller into ESMPro Dataviewer ? |
| --- | --- |
| Document ID: | TID0612041603 |
| Creation Date: | 4 Dec. 2006 |
| Modified Date: | 8 Jan. 2008 |
| Document Revision: | 3 |
| Product Class: | Servers |
| Product and Version: | ESMPro integration |

Warning

On server systems installed with ESMPro Agent, MSM events will be integrated automatically in order to have RAID events sent to ESMPro Manager Alert Viewer.
Note: make sure to use the latest version of ExpressBuilder to have up to date version of ESMPro Agent and MSM.

ESM Disk Array is a module adding RAID controller, physical and logical in ESMPro Dataviewer. ESM Disk Array doesn’t support LSI based SATA and SAS controller yet. This document is not supposed to replace ESM Disk Array. This is only a workaround in order to have a Server Icon color change into Operation Windows and Dataviewer in case of disk failure (real time monitoring)

Hardware and Operating System Supported

LSI Card used on NovaScale R400, R600 and T800 series by this TID:

MegaRAID SAS 8408E

MegaRAID SAS 8480E

MegaRAID SAS 8300XLP

MegaRAID SAS 8704ELP

MegaRAID SAS 8708EM2

On board SATA in RAID mode: controller ESB2 with Stack LSI (CTRL+M)

On board SAS in RAID mode: controller 1068 with Stack LSI (CRTL+M)

No SCSI

Operating System

Windows Server 2003 x32 and x64

Linux Suse and RedHat

Requirement

- Server installed with its ESMPro Agent and properly discovered under ESMPro Manager.

- ESMPo Agent set to report alert by TCP/IP In-Band to ESMPro Manager

- SNMP service on Manager Server has to be in ‘READ-CREATE’ access.

- Package (below) including LSI SNMP Agent and its MIB
(Notice: in previous release of this TID, another MIB was integrated because original LSI MIB was not compatible with ESMPro, with new version of LSI SNMP, the new MIB is compliant with ESMPro)

Installation

- On server to be monitored, (server with LSI controller and ESMPro Agent), install LSI SNMP agent provided below:

  - For Linux, see SAS_SNMP_Linux_Installer-3.11-0003.zip

  - For Windows, SAS_SNMP_Win_Installer-3.13-0002.zip

- On manager server (server with ESMPro Manager), import LSI MIB file “LSI-AdapterSAS.mib“ provided in the ZIP file used previously.
Follow the screen shots and pay attention to mouse cursor

As described, server has to be restarted.

- On manager server, open Dataviewer of server to be monitored, click LocalPolling Click on first line of “Polling Target” and click on “Configure…”,

- Follow the next screen shot and pay attention to mouse cursor

- Fill line “Object ID” and “Comment” with following values:

Object ID: 1.3.6.1.4.1.3582.4.1.4.1.2.1.19

Comment: LSI_VD_DEGRADED_COUNT

Note: This OID is a counter giving the amount of logical drives with “degraded” status. Bull recommend to monitor this OID because it is insuring that data redundant. Other counters can be added by investigating LSI MIB file.

- Close the window by OK

- On following screen check: “Enable Polling”, “Enable Sending Trap” and fill “Major Upper / Upper Reset, Minor Upper / Upper Reset” as described:

- When you click on OK, return to “Local Polling”, make sure the pair of glasses appear as follow

Test

- Switch a Virtual Drive to degraded by putting one of the physical drive Offline using MSM software.

- As a result, Item entry in LocalPolling should switch to warning (=yellow color):

And Alert should arrive on Alertviewer

Package

Version History

Version 3.0:

- Add list of Hardware and Operating System supported.

- Update to new LSI SNMP Agent

| Document owner: | COE Servers |
| --- | --- |
| Applies to: | See Hardware supported part |

# Text boxes

Technical Information Document

COE

Servers