BIOS for Novascale Universal R423

bought with Redhat/XBAS or without Operating System.

Release Notes

R4230X60.IMG (2008-November-20)

This version has been built with the official package 7DWNB048.exe (2008/11/19)

It contains the BIOS Rev. 1.2 for X7DWN+

Bios improvements: To see : ECO_12683.889.1.pdf

- Fix IPMI connection may be broken in system reset (ALL)

- Fix system configuration data is not updated to IPMI if power on system 1 minute after AC cable applied (ALL)

- Fix SLP2 code is conflict with WHEA code (ALL)

- Fix CPU in socket 0 is not selected as BSP sometimes (ALL)

- Update AHCI firmware from 1.17D to 1.20E (ALL)

- Fix USB keyboard cannot work when USB sound device is installed (ALL)

- Fine tune PCI Express init timing (ALL)

- Change Max Payload Size algorithm (ALL)

- Change Crystal Beach to I/OAT2 (ALL)

- Enable HPET by default (ALL)

- Fix CF card bootable issue (ALL)

- Fix SLP2 code is conflict with WHEA code (ALL)

R4230X40.IMG (August 14, 2008)

This version has been built with the official package 7DWN8048.EXE

In contains the official BIOS Rev. 1.1b  X7DWN+ dated from 08/04/08.

It supports the INTEL Harpertown processor with stepping E-0.

R4230X30.IMG, May 21, 2008

This version has been built with the official package 7DWN4308.exe but it contains the Beta version

7DWN4308.ROM (sent by J.Miranda) to correct the problem encountered with 64GB(*) of memory (the checking of the memory was too long and all the capacity was not available).

(*)(16x   FBD DDR2-1.8v-800MHz   Hynix  4GB  HYMP151F72CP4D3-S5 and 2 processors Intel Xeon E5462)

In this version

Setup Parameters.Advanced.Boot Features.QuickBoot Mode   = Enabled

.

R4230X23.IMG

Same as version R4230X22.IMG but

Setup.Advanced.Boot Features.Power Loss Control = Stay Off instead of Last State

Support of the RAID HBA AOC-USASLP-S8iR in the boot list.

R4230X22.IMG

Same as version R4230X21 for the BIOS itself and the options of SETUP.

The difference is the possibility provide to the operator to enter or not the DMI String : system-serial-number,.

Examples :

FB	XAN-SM7-00012

( Reset the DMI strings and set the values of the image overloading by the options of the command phlash16.

FB

( Don’t reset the DMI strings, keep the old values overloading them with the options of the command phlash16.

Read the difference /mode=  of the command phlash16.exe

Other difference :

The tools IPNMAC.EXE and IPMICFG.EXE were add to the diskette so that the operator can insert the IP address of the l’AOC-SIMSO[+].

# Text boxes

R4230X60            November 20, 2008

Novascale R423

(X7DWN+)

Flash BIOS 7DWNB048.exe

« R4230X60.ROM»

with Logo Bull

Built with Phoenix BIOS Editor 2.2.0.9

BIOS Rev. 1.2 X7DWN+ (2008/11/19)

Write enable

no hole